## Slide 1: Preliminary Zn(n,p)Cu Data
Andrew Voyles
22 February 2016

## Slide 2: Experimental Setup – 03 Nov 2015
Zinc
  Thickness: 1.03 ± 0.01 mm
  Diameter: 9.90 ± 0.15 mm
  Weight: 0.5375 ± 0.0001 g
Indium
  Thickness: 0.48 ± 0.02 mm
  Diameter: 9.77 ± 0.12 mm
  Weight: 0.2475 ± 0.0001 g
Beam On: 2:13:16 PM
Beam Off: 5:13:16 PM
Start of Counting: 5:43:01 PM
Polyethylene
Indium
Zinc

## Slide 3
336 keV - 115m In IT Decay
391 keV - 113m In IT Decay
417 keV - 116 In β- Decay
511 keV - 64 Cu β+ Decay

## Slide 4
336 keV - 115m In IT Decay
391 keV - 113m In IT Decay
417 keV - 116 In β- Decay
511 keV - 64 Cu β+ Decay
Background Subtracted

## Slide 5: Fitting to Model

## Slide 7: Results
 | T ½ (ENSDF) | T ½ (Measured) |  |  |  | Χ^2/DoF | #σ above ENSDF
Counts (336 keV) | 4.486 h | 4.519 | ± | 0.0457 | h | 1.7286 | 0.722
Counts (391 keV) | 99.476 m | 104.5208 | ± | 5.6701 | m | 1.721 | 0.890
Counts (417 keV) | 54.29 m | 52.0074 | ± | 2.6139 | m | 1.021 | -0.873
Counts (511 keV) | 12.701 h | 11.8183 | ± | 0.7027 | h | 1.6785 | -1.256

## Slide 8
Qβ = 3.278 MeV

## Slide 9: Experimental Setup – 11 Feb 2016
Zinc
  Thickness: 1.03 ± 0.01 mm
  Diameter: 9.85 ± 0.15 mm
  Weight: 0.4514 ± 0.0001 g
Indium
  Thickness: 0.51 ± 0.02 mm
  Diameter: 9.786± 0.12 mm
  Weight: 0.2481± 0.0001 g
Beam On: 2:40:30 PM
Beam Off: 6:02:00 PM
Start of Counting: 6:37:25 PM
Polyethylene
Indium
Zinc

## Slide 10
Qβ = 3.278 MeV

## Slide 11
Qβ = 3.278 MeV

## Slide 12
Qβ = 3.278 MeV

## Slide 13: Results – Removal of 511 Contamination
 | T ½ (ENSDF) | T ½ (Measured) |  |  |  | Χ^2/DoF | #σ above ENSDF
Counts (336 keV) | 4.486 h | 4.519 | ± | 0.0457 | h | 1.7286 | 0.722
Counts (391 keV) | 99.476 m | 104.5208 | ± | 5.6701 | m | 1.721 | 0.890
Counts (417 keV) | 54.29 m | 52.0074 | ± | 2.6139 | m | 1.021 | -0.873
Counts (511 keV) (cut 1st 4hrs ) | 12.701 h | 12.0791 | ± | 1.0704 | h | 1.7616 | -0.581
Counts (511 keV) (11 Feb Run) | 12.701 h | 11.8804 | ± | 0.8377 | h | 1.1299 | -0.980

## Slide 14: 67Cu Peaks – 80 hrs into count
184.5 keV - 67 Cu β- Decay

## Slide 15: Next Steps
Need to apply correct detector efficiency calibration
  Will not affect half lives of peaks, just XS calculations
  Calculate 64Cu production XS, relative to In
  XS appears to be ~50 mb
Preparing for (n,p) measurements on:
  50Ti(n,α),47Ca
  105Pd(n,p)105Rh
  159Tb(n,p)159Gd
Extend measurements to En ≤ ~55 MeV, using 88” Cyclotron 7Li(p,n) quasi-monoenergetic neutron source (currently in development with Jon Engle [LANL])
Measure 67Cu production cross section using LEPS
  184.5 keV peak masked by U/Pb decay chain, Compton background
  Also inhibited by lower production XS
  Use enriched 67Zn target?