## Slide 1: Preliminary Zn(n,p)Cu Data
Andrew Voyles
30 November 2015
HFNG Meeting Update

## Slide 2: Experimental Setup – 03 Nov 2015
Zinc
  Thickness: 1.03 ± 0.01 mm
  Diameter: 9.90 ± 0.15 mm
  Weight: 0.5375 ± 0.0001 g
Indium
  Thickness: 0.48 ± 0.02 mm
  Diameter: 9.77 ± 0.12 mm
  Weight: 0.2475 ± 0.0001 g
Beam On: 2:13:16 PM
Beam Off: 5:13:16 PM
Start of Counting: 5:43:01 PM
Polyethylene
Indium
Zinc

## Slide 3
336 keV - 115m In IT Decay
391 keV - 113m In IT Decay
417 keV - 116 In β- Decay
511 keV - 64 Cu β+ Decay

## Slide 4: Fitting to Model

## Slide 6: Results
 |  | T ½ (ENSDF) | T ½ (Measured) |  |  |  | Χ^2/DoF
115m In IT Decay | Counts (336 keV) | 4.486 h | 4.519 | ± | 0.0457 | h | 1.7286
113m In IT Decay | Counts (391 keV) | 99.476 m | 104.5208 | ± | 5.6701 | m | 1.721
116 In β Decay | Counts (417 keV) | 54.29 m | 55.9695 | ± | 1.0524 | m | 1.0927
64 Cu β+ Decay | Counts (511 keV) | 12.701 h | 11.8183 | ± | 0.7027 | h | 1.6785

## Slide 7: Commentary
Assumed zero baseline counts, to minimize χ2
~0.5-1.0 keV drift of the peak centroids from expected energies, even after energy calibration.
Broad 511 peak
  FWHM: 3.1-3.6 keV, others have 1.5-1.6 keV
3/4 of the ENSDF half-lives not falling within 1 standard deviation (95% CI) of the measured values.
  But just barely…
Need to apply detector efficiency calibration
  Will not affect half lives of peaks, just XS calculations
Next priority: Calculate 64Cu production XS, relative to In