## Slide 1: ​Cross-Section Measurements for Novel Medical Radionuclides at UCB/LBNL: The Challenge of "Simple" Experiments
Andrew S. Voyles
12 February 2018 – NE Department Colloquium

## Slide 2: Overview
Background & history of nuclear medicine
64Cu and 47Sc (n,p) cross-section measurements
Stacked-target charged particle excitation functions
Path forward

## Slide 3: Background & History of Nuclear Medicine
___________________________

## Slide 4: Nuclear Medicine in the U.S.
[1] C. Whipple and S. Larson, Medical Isotope Production Without Highly Enriched Uranium, 2009.
[2] United States Government Accountability Office and U.S. General Accounting Office, Report GAO-08-452,2008.
[3] A. N. Khalid, et al, “Arch. Otolaryngol. Neck Surg., vol. 132, no. 3, pp. 244–250, 2006.
Nearly 17M procedures performed annually in the US
Major isotopes in modern clinical nuclear medicine:
  99mTc
    Diagnostic isotope for cardiac, renal, lung function, tumor imaging
    Produced as fission product in thermal reactors
    Costs per 10-mCi dose ranges $20-401
  18F
    PET isotope used for metabolic tumor & metastasis imaging
    Produced by K~15 medical cyclotrons via 18O(p,n)18F
    Costs per 5-mCi dose ranges $400-8002
  131I
    β-therapy isotope used for treatment of cancers, including thyroid and neuroendocrine
    Produced as fission product in thermal reactors
    Costs per 200-mCi dose approximately $2003
Notes: Dates back to 1946 – 14C production at ORNL Graphite Reactor1
Per the US Society of Nuclear Medicine & Molecular Imaging, approximately 17 million nuclear medicine (diagnostic and therapeutic, on top of another ~130M of radiology) procedures are performed in the US annually
  Nearly 1 in 20 people!
  Annual industry estimated at $2.4 B

## Slide 5: Nuclear Medicine in the U.S.
Established medical radioisotopes face several challenges:
  Non-ideal decay properties for desired application
    Extra dose
    Extra range
  Curtailment of production facilities (99mTc)
  Thermal reactor issues
    Low yield
    Difficult radiochemical purification
    Feasibility & deployability
Why do we keep doing this?
How can we improve this?

## Slide 6: Nuclear Medicine in the U.S.
Established medical radioisotopes face several challenges:
  Non-ideal decay properties for desired application
    Extra dose
    Extra range
  Curtailment of production facilities (99mTc)
  Thermal reactor issues
    Low yield
    Difficult radiochemical purification
    Feasibility & deployability
Why do we keep doing this?
How can we improve this?
…and new paradigms for isotope production!
Novel isotopes…

## Slide 7: Some perspective
S.M. Qaim
Notes: Dr Qaim - plenary speaker and instigator of priority isotopes

## Slide 8: Some perspective
NDNCA Whitepaper available at http://bang.berkeley.edu/events/ndnca/whitepaper/
Highlight from WTTC 2016: 54Fe(p,α)51Mn

## Slide 9: Some perspective
Emerging trends for next-generation (targeted & personalized) nuclear medicine:
  Targeted alpha therapy (5-10 MeV)
    40-80 μm range  single cell
  Targeted Auger therapy (20 eV – 1 keV)
    1 nm – 2 μm  cellular nucleus
  Theranostic medicine
    Simultaneous imaging and therapy
Notes: DOE-NP has long-range plan to pursue development of these emerging isotopes

## Slide 10: Overview
Ongoing targeted experimental campaign to address these needs:
  (n,p) production cross sections – UCB
  Stacked-target charged particle excitation functions
    Low energy – LBNL
    Moderate energy – LANL
    Bonus – spin distribution of excited nuclear states

## Slide 11: The LBNL/UCB Bay Area Nuclear Data (BAND) Group*…
A. Lewis
A. Springer
J. Batchelder
M. Basunia
A. Hurst
L. Kirsch
E. Browne
Our goal is to address the data needs of the applied nuclear science community while training the next generation of nuclear scientists and engineers in the process
L. Bernstein
E. Matthews
UCB Nuclear Engineering students lead our experimental program
J. Morrell
A. Voyles
Notes: We do this by bringing together young…and other…scientists and engineers

## Slide 12
UC Berkeley
LBNL
LLNL
LANL
University of Iowa
University of Wisconsin - Madison
University of Oslo
University of Lahore
Karlsruhe Institute of Technology
Forschungszentrum Jülich

## Slide 13: A simple picture of cross-sections…
Proper characterization of is often the largest source of uncertainty in precision measurements
Notes: Many XS measurements fail to report an energy uncertainty!

## Slide 14: 64Cu and 47Sc (n,p) Cross-Section Measurements
___________________________

## Slide 15: Medical Applications
Emerging medical radionuclides
  64Cu (t1/2 = 12.7 hr) – 61% β+ to 64Ni, 39% β- to 64Zn
  47Sc (t1/2 = 3.35 d) – β- to 47Ti, with 159-keV γ

## Slide 16: Why (n,p) via DD neutrons?
Advantages over thermal reactors:
  Co-production of many unwanted activities via (n,γ)
  Far cheaper startup costs, no proliferation concerns
Advantages over DT neutrons:
  14-15 MeV DT neutrons open up unwanted (n,pxn) channels, contaminating the desired product
  No tritium handling concerns
2-3 MeV DD neutrons are ideal for (n,p) and (n,α) production, but often suffer from fairly low flux, and poor nuclear data

## Slide 17: The UC Berkeley High Flux Neutron Generator
Deuterium Gas
RF
D Plasma
100kV
D beam
1-1000mA
DD Fusion
2.45 MeV neutrons, 107 n/s/cm2
Extraction Plate: 5mm diameter
H2O

## Slide 18
J. Morrell
M. Unzueta
C. Waltz
3 generations of our “real neutron source”

## Slide 19: The UC Berkeley High Flux Neutron Generator
Foils Used | Metal Purity | Abundance (a/o) | Foil Density (mg/cm2)
natIn | > 99.999% | 113In (4.29%), 115In (95.71%) | 365.5
natZn | > 99.99% | 64Zn (49.17%) | 714.1
natTi | 99.999% | 47Ti (7.44%) | 450.6
Dosimetry: IRDFF 113/115In(n,n’)113m/115mIn standards
Notes: 64Zn - 49.17%, 66Zn – 27.73%, 67Zn – 4.04%, 68Zn – 18.45%
46Ti – 8.25%, 47Ti – 7.44%, 48Ti – 73.72%, 49Ti – 5.41%, 50Ti – 5.18%

## Slide 20: The UC Berkeley High Flux Neutron Generator
Zn
In
Zn
In

## Slide 21
Relative Activation Measurements

## Slide 22
Relative Activation Measurements
t1/2 = 4.519 ± 0.016 h
(Accepted = 4.486 h)
χ2 /ν = 1.653
t1/2 = 12.10 ± 0.85 h
(Accepted = 12.701 h)
χ2 /ν = 1.743
Notes: Producing O(10 kBq), with dead time < 5%

## Slide 23
Neutron Energy Spread
Titanium
D
d
n
n
n
n
θ

## Slide 24
Neutron Energy Spread
Neutron Energy Spread
Relative fluxes as seen by a 3 x 3 array of 0.5-cm diameter indium foils. The central foil corresponds to the location in which target and monitor
foils were mounted during the cross section measurements, verifying
that the beam is centered on the middle of mounted foils

## Slide 25
Neutron Energy Spread
H. Liskien et al., Nucl Data Tables, vol 11, 2973
Neutron Energy Spread
Neutron flux profile modeled in target and monitor foil, using MCNP6
Emax = Maximum energy neutron subtended by foil
F(E’) = Fraction of Total Reactions induced up to energy E’
<E>
+σ<E>
-σ<E>

## Slide 26
Neutron Energy Spread
64Zn(n,p)64Cu
47Ti(n,p)47Sc
47Ti(n,p)47Sc
“Measurement of the 64Zn, 47Ti(n,p) cross sections using a DD neutron generator for medical isotope studies”, Nuclear Instruments and Methods in Physics Research B 410 (2017) 230–239

## Slide 27
Neutron Utilization
Theoretical saturation activities are currently estimated at 1.5 kBq of 64Cu, 0.11 kBq of 47Sc
  Characterizes the effectiveness of a neutron generator as an isotope generator
  Measured production rates were 453.8 Bq of 64Cu, 31.6 Bq of 47Sc
  Implies η ≈ 3 x 10-5 (64Cu), η ≈ 1 x 10-5 (47Sc)

## Slide 28: Measurement of the 98Mo(n,γ) Cross Section
A recent experiment at the HFNG was conducted by Eric Matthews to re-measure the (n,γ) cross section of 98Mo.
Using a custom target holder, four energy locations were measured.
This cross section has not been measured since 1967 and re-measurement of this cross section in the 1-10 MeV was marked as a vital nuclear data need in the NDNCA nuclear data needs matrix, for thermal reactor 99Mo production.
Stupegia et al., 1967

## Slide 29: Stacked-target Charged Particle Excitation Functions
___________________________
Low Energy – LBNL

## Slide 30: Why charged particle production?
Cyclotron
  Many hospitals have small K~15 medical cyclotrons for PET tracer production
  Leverage existing infrastructure
  Explore higher energies for regional research cyclotrons, basic science
Linac
  Commonly used for high-energy production (LANL – IPF)
  Useful for anchoring to complementary low-energy measurements

## Slide 31
Emerging medical radionuclides
  51Mn (t1/2 = 46 min, 97% β+) – short-lived PET tracer for metabolic studies
  52gMn (t1/2 = 5.6 d, 29% β+) – long-lived PET tracer for neuron tracking, immune studies
  Manganese has well-established biochemistry and uptake via DOTA-based chelation
51,52Mn - Motivation
Mn
Mn
  Almost no Fe(p,x) XS measurements exist – can use these to probe spin physics in the A≈50 region
Notes: The four secondary amine groups are modified by replacement of the N-H centers with N-CH2CO2H groups. The resulting aminopolycarboxylic acid, upon ionization of the carboxylic acid groups, is a high affinity chelating agent for di- and trivalent cations.

## Slide 32
Methodology
K-140
Notes: Cyclotron freq w = Q B / m
T = (m/2) w^2 r^2
T/A = (B r / 2 m)^2 (Q/A)^2 = K (Q/A)^2

## Slide 33
  Two overlapping stacks: Ep= 5521 MeV, 2511 MeV
  (120 nA@10 min, 100 nA@20 min)
L. Bernstein
A. Springer
2.5 cm

## Slide 34
25 μm-thin natFe, natCu, natTi foils in 0.1” Al frames
Dosimetry: IAEA charged particle beam monitor reactions:
  natTi(p,x)48V
  natCu(p,x)62,63,65Zn
  nds.iaea.org/medical/monitor_reactions.html
2.5 cm
Energy Sensitivity
Fluence Sensitivity

## Slide 35
Fe(p,x)
Ti(p,x)
Cu(p,x)

## Slide 36
Data Analysis Issues
Why is no activity seen in Ti20 / Cu20?

## Slide 37
Notes: Monitor foils as “canary in the coal mine”

## Slide 38
Silicone Adhesive
Silicone Adhesive
Corrected Energy Assignments
Activation Foil
Kapton
Kapton
25 μm @1.42 g/cm3 = 3.55 mg/cm2
25 μm = 11 - 23 mg/cm2
38 μm @1.18 g/cm3 = 4.48 mg/cm2
25 μm @1.42 g/cm3 = 3.55 mg/cm2
38 μm @1.18 g/cm3 = 4.48 mg/cm2

## Slide 39
Corrected Energy Assignments

## Slide 40
S. A. Graves, P. A. Ellison, T. E. Barnhart, H. F. Valdovinos, E. R. Birnbaum, F. M. Nortier, R. J. Nickles, and J. W. Engle, Nucl. Instruments Methods Phys. Res. Sect. B Beam Interact. with Mater. Atoms, vol. 386, pp. 44–53, Nov. 2016.
LANL sees the same issue…

## Slide 41
Corrected Energy Assignments
Goal: Minimize standard deviation of

## Slide 42
Preliminary
Using current from charge integrator
Notes: Discrepancy possible causes :
Still using current from charge integrator, once energy assignment is finished, monitor foils will provide renormalization to true current
Direct production of 51Cr creates “extra” cross section
Low peak is 54Fe(p,x), high peak is 56Fe(p,x)

## Slide 44
Preliminary

## Slide 45
  Results consistent with R≈1 at high energy.
  At low energy, results are ambiguous due to energy straggling.
Preliminary

## Slide 46
Spin Distribution Application
Through its impact on nuclear level densities, the spin cut-off parameter has a strong impact on the favoring of higher-spin isomers in charged particle-induced reactions – a “tuning parameter” for isomer-to-ground state branching ratio
  Reaction physics codes can be used to model (σm/σg) when experimental data is unavailable
  Case study: 177Lu
    177gLu (t1/2 = 6.7 d) – emerging β- therapy agent
    177mLu (t1/2 = 160 d) – contributes extra dose to patient, without therapeutic or diagnostic benefit
    Improved spin distribution measurements can improve modeling to guide production studies

## Slide 47: Stacked-target Charged Particle Excitation Functions
___________________________
Moderate Energy – LANL

## Slide 48: Measurements @ LANL – Nb(p,x)
natNb(p,4n)90Mo is a high-priority objective as a new proton beam dosimetry standard for Ep ≈ 50 – 100 MeV
  Other emerging radionuclides: 82mRb, 86Y, 89Zr, 90Nb
ε+β+ |  |  | 90Mo |  |  | 93mMo | 94Mo | 
IT |  |  | 89mNb 89Nb | 90Nb | 91mNb | 92mNb | 93Nb | 
 | 86Zr | 87Zr | 88Zr | 89Zr |  |  |  | 
 | 85mY 85Y | 86Y | 87mY 87Y | 88Y |  |  |  | 
83Sr |  | 85mSr |  |  |  |  |  | 
82mRb |  |  |  |  |  |  |  | β-
100 MeV p+
N
Z

## Slide 49: Measurements @ LANL – Nb(p,x)
Proton Injectors
p+
p-
750 keV
100 MeV
800 MeV
To research centers
201.25 MHz Drift Tube Linac
IPF
805 MHz Side-Coupled Cavity Linac
800 m
p-
p+
h+

## Slide 50: Measurements @ LANL – Nb(p,x)
LBNL: 5 – 55 MeV / A, LANL: 45 – 100 MeV p+
Complementary measurements explore reaction dynamics in different energy regimes, overlap region of 45-55 MeV builds confidence and consistency in results.
100 MeV p+
M. Nortier
100 nA @ 3 hr

## Slide 51
Measurements @ LANL – Nb(p,x)

## Slide 52
Measurements @ LANL – Nb(p,x)
1894 unique peaks across 107 spectra

## Slide 53
Better consistency…but why is 22Na so high?

## Slide 54
Silicone Adhesive
Silicone Adhesive
It’s always the Kapton!
Activation Foil
Kapton
Kapton
25 μm @1.42 g/cm3 = 3.55 mg/cm2
25 μm = 11 - 23 mg/cm2
38 μm @1.18 g/cm3 = 4.48 mg/cm2
25 μm @1.42 g/cm3 = 3.55 mg/cm2
38 μm @1.18 g/cm3 = 4.48 mg/cm2

## Slide 56
Measurements @ LANL – Nb(p,x)
A.S. Voyles et al., “Measurement of nuclear excitation functions for proton induced reactions (Ep = 40 – 90 MeV) on natural Nb and Cu”, PRC 2018 (in preparation)
38 measurements of cross-sections for 93Nb(p,x) and natCu(p,x)

## Slide 57
Measurements @ LANL – Nb(p,x)
5 independent measurements of isomer-to-ground state ratios
A. Lewis

## Slide 58
Provides first / vastly improved production measurements for each of the isotopes listed here
Thin-target measurements in this work provide an ideal jumping-off point to begin thick-target yields for commercial application, as well as radiochemical workup
Demonstrated ability to measure excitation functions for emerging medical radionuclides through 3 different production paradigms
S. Siem
G. Henriksen
B. Schoultz

## Slide 59
Path Forward: 238U(p,xn)236,237Np and 235U(d,x)236Np Production
Literature reaction cross sections for 238U(p, xn)
green x=1
brown x=3
blue x=4
Vital mass-spec “spike” for nonproliferation

## Slide 60: Path Forward: 7Li(p,n) “Quasi-Monoenergetic” Neutron Source
Neutrons from 0-60 MeV
Samples irradiated in the vault
Unreacted beam dumped in Cave 0
Flux from 106-4 /MeV/sr/s (decreases w/En)
First experiments are planned for April 2018
Li(p,n) neutron
production target
Inconel-clad Li targets
(LANL LDRD)
Jon Engle
Unreacted protons
Vault-based irradiation
0°
-20°
Notes: This is the same method used at the new FRANZ facility in Frankfurt.

## Slide 61: Path Forward: 140La(p,6n)134Ce as a PET tracer for 225Ac
Stacked Target Holder
HPGe counter
Jon Morrell
140La(p,6n)134Ce Cross Section
Preliminary
Kratochwil, Clemens, et al. "225Ac-PSMA-617 for PSMA-targeted α-radiation therapy of metastatic castration-resistant prostate cancer." Journal of Nuclear Medicine 57.12 (2016): 1941-1944.
Investigating potential for 226Ra(2,2n)225Ra  225Ac
Notes: 3x 9 MBq dose fractions

## Slide 62: Collaborators on this work
M.S. Basunia1, J.A. Batchelder2, J.D. Bauer3, T.A. Becker4, L.A. Bernstein1,2, E.R. Birnbaum5, J.W. Engle5,6, R.B. Firestone1, S.A. Graves7, G. Henriksen8, A.M. Hurst1, L. Kirsch3, A.M. Lewis2, E.F. Matthews2, F.M. Nortier5, S.M. Qaim9, P.R. Renne4, D. Rutte4, B.W. Schoultz10, S. Siem11, A. Springer12, M.A. Unzueta2, K.A. Van Bibber2, A.S. Voyles2, C.S. Waltz3 H. Zaneb13
1 Lawrence Berkeley National Laboratory
2 University of California-Berkeley Dept. of Nuclear Engineering
3 Lawrence Livermore National Laboratory
4 Berkeley Geochronology Center
5 Los Alamos National Laboratory
6 University of Wisconsin – Madison
7 University of Iowa – Department of Radiation Oncology
8 University of Oslo – Institute of Basic Medical Sciences
9 Forschungszentrum Jülich
10 University of Oslo – Department of Chemistry
11 University of Oslo – Department of Physics
12 Karlsruhe Institute of Technology
13 University of Lahore