## Slide 1: Isotope Production Activities at LBNL and LANSCE-IPF: Development of a new Nb(p,x)90Mo Monitor Reaction and Fe,La(p,x) Production Cross-Section Measurements
Andrew S. Voyles
30 August 2018 – 17th International Workshop on Targetry and Target Chemistry
Notes: Emerging trends for next-generation (targeted & personalized) nuclear medicine:
  Targeted alpha therapy (5-10 MeV)
    40-80 μm range  single cell
  Targeted Auger therapy (20 eV – 1 keV)
    1 nm – 2 μm  cellular nucleus
  Theranostic medicine
    Simultaneous imaging and therapy

## Slide 2: Stacked-target Charged Particle Excitation Functions
___________________________
Intermediate Energy – LANL

## Slide 3: Measurements @ LANL – Nb(p,x)
M. Nortier
Well-characterized monitor reaction data is a top-priority objective
    Vital for determination of fluence, energy for isotope production
    Current data are deficient for Ep>30 MeV
  A stacked target measurement was run at LANSCE-IPF to help develop the 93Nb(p,4n)90Mo reaction as a new 30-200 MeV proton standard
Proton Injectors
p+
p-
750 keV
100 MeV
800
MeV
201.25 MHz Drift Tube Linac
IPF
805 MHz Side-Coupled Cavity Linac
800 m
p-
p+
[1] A.S. Voyles, NIM B 429 (2018)

## Slide 4: Measurements @ LANL – Nb(p,x)
A.S. Voyles et al., “Excitation functions for (p,x) reactions of niobium in the energy range of Ep = 40–90 MeV”, NIM B 429 (2018) 53–74. June 2018
Measurements of 38 cross-sections for 93Nb(p,x) and natCu(p,x)
Pathway for medical radionuclides: 82mRb, 86Y, 89Zr

## Slide 5: Measurements @ LANL – Nb(p,x)
5 independent measurements of isomer-to-ground state ratios
[1] A.S. Voyles, NIM B 429 (2018)

## Slide 6: Measurements @ LANL – Nb(p,x)
[1] A.S. Voyles, NIM B 429 (2018)
“Excess” fluence seen in 22,24Na consistent with production via Si(p,x)

## Slide 7: Stacked-target Charged Particle Excitation Functions
___________________________
Low(er) Energy – LBNL
Notes: Cyclotron
  Many hospitals have small K~15 medical cyclotrons for PET tracer production
  Leverage existing infrastructure
  Explore higher energies for regional research cyclotrons, basic science
Linac
  Commonly used for high-energy production (LANL – IPF)
  Useful for anchoring to complementary low-energy measurements

## Slide 8: Stacked-target Charged Particle Excitation Functions
K-140
L. Bernstein
A. Springer
2016: Launched a complementary nuclear data measurement campaign at the LBNL 88-Inch cyclotron to address gaps in reaction data at E<60 MeV/A
Notes: We propose to measure these reactions to resolve ambiguity in the predictions and establish optimal irradiation parameters.
Cyclotron freq w = Q B / m
T = (m/2) w^2 r^2
T/A = (B r / 2 m)^2 (Q/A)^2 = K (Q/A)^2

## Slide 9: natFe(p,x)51,52Mn – Novel PET imaging
Preliminary
Preliminary
Emerging medical radionuclides
  51Mn (t1/2 = 46 min, 97% β+) – short-lived PET tracer for metabolic studies
  52gMn (t1/2 = 5.6 d, 29% β+) – long-lived PET tracer for neuron tracking, immune studies
Two overlapping stacks: Ep= 5515 MeV, 250 MeV (120 nA@10 min, 100 nA@20 min)
Notes: Mention issues with Levkovski!
Low peak is 54Fe(p,x), high peak is 56Fe(p,x)

## Slide 10: 140La(p,6n)134Ce - a PET analogue for 225Ac
Jon Morrell
[2] Kratochwil, Clemens, Journal of Nuclear Medicine 57.12 (2016).
Th4+
Ce4+
Ac3+
Ce3+
Ce
-e1-
+e1-
134Ce as a 227Th mimic
134Ce as an 225Ac mimic
225Ac decay chain lacks sufficient positrons to produce a signal that can be detected by PET.
  In order to employ PET to explore new uses of alpha emitters, positron-emitting, surrogate radionuclides will have to be developed.
  134Ce/134La: t1/2 = 75.9 h / 6.67 m, 2.7 MeV β+ (62.0%)
Cross sections un-measured and reaction modeling predictions (EMPIRE/TALYS) differ by >10x
Notes: 3x 9 MBq dose fractions
Useful for bio-kinetic studies of monoclonal antibodies (the delivery agent)
Interesting nuclear physics relevance: pre-equilibrium modelling, isomer/ground state ratios
No previous measurements, only comparison to models
Surprising results: TALYS 10x over-prediction of XS

## Slide 11: 140La(p,6n)134Ce - a PET analogue for 225Ac
135Ce is major contaminant: higher-energy ≈70 MeV beam required for clean production of 134Ce
TALYS and ALICE overpredict (p,6n) cross section by >10x, XS peaks 8-10 MeV higher than predicted
Reaction code differences: Hybrid Monte-Carlo pre-equilibrium (EMPIRE) vs. Exciton model (TALYS, ALICE)
Notes: 3x 9 MBq dose fractions
Useful for bio-kinetic studies of monoclonal antibodies (the delivery agent)
Interesting nuclear physics relevance: pre-equilibrium modelling, isomer/ground state ratios
No previous measurements, only comparison to models
Surprising results: TALYS 10x over-prediction of XS

## Slide 12: 140La(p,6n)134Ce - a PET analogue for 225Ac
MCNP6 Energy Assignment
Anderson & Ziegler Energy Assignment
Major takeaways:
Significant deviation (>20%) between Anderson & Ziegler and MCNP6/X
  Future work: explore in depth with other stacked target data
La metal targetry concerns:
  Significant decomposition, outgassing post-EoB
Notes: Next steps:
Extension to 100 MeV using LANSCE-IPF in October 2018
Radiochemical separation and bio-uptake studies with LBNL/LANL – TTA extraction of Ce(IV) from La(III), followed by anion exchange to remove La target material

## Slide 13: Collaborators on this work
M.S. Basunia1, L.A. Bernstein1,2, E.R. Birnbaum3, J.W. Engle3,4, S.A. Graves5, T. Kawano3, A.M. Lewis2, E.F. Matthews2, J.T. Morrell2, F.M. Nortier3, A. Springer6, A.S. Voyles2
1 Lawrence Berkeley National Laboratory
2 University of California-Berkeley Dept. of Nuclear Engineering
3 Los Alamos National Laboratory
4 University of Wisconsin – Madison
5 University of Iowa – Department of Radiation Oncology
6 Karlsruhe Institute of Technology
We gratefully acknowledge support from:
U.S. Department of Energy, Office of Science via the Isotope Development and Production for Research and Applications subprogram in the Office of Nuclear Physics
Lawrence Berkeley National Laboratory and the U.S. Nuclear Data Program under contract # DE-AC02-05CH11231
U.S. Nuclear Regulatory Commission
U.S. Department of Energy grant #DE-SC0019238 – Support for Students, Postdoctoral Fellows, and Trainees to Attend the 17th International Workshop on Targetry and Target Chemistry

## Slide 14: Questions?

## Slide 15: The LBNL/UCB Bay Area Nuclear Data (BAND) Group
A. Lewis
J. Batchelder
M. Basunia
N. Petterson
R. Firestone
Our goal is to address the data needs of the applied nuclear science community while training the next generation of nuclear scientists and engineers in the process
L. Bernstein
E. Matthews
UCB Nuclear Engineering students lead our experimental program!
J. Morrell
A. Voyles
I. Kolaja
K. Song
Camera Shy: E. Browne, A. Hurst
Notes: We do this by bringing together young…and other…scientists and engineers

## Slide 18: Simultaneous Radionuclide Production
[1] K. P. Harrig, et al., “Neutron Spectroscopy for pulsed beams with frame overlap using a double time-of-flight technique,” NIM A, 877, pp. 359–366, 2018.
(d,xn) target
Thick Be breakup target
≤ 50 MeV deuterons
Unreacted deuterons
Energetic secondary neutrons
(n,p) and/or (n,2n) target
(d,xn) reactions can produce the same radionuclide as commonly-used (p,n)
Simultaneously makes a significant energetic secondary neutron flux (ESNF) from breakup of unreacted primary deuteron beam.
ESNF can be used to produce high specific-activity radionuclides via (n,2n), or charge exchange reactions such as (n,p) and (n,α).
235U(d,n)236Np w/ Zn(n,p)64,67Cu measured in August 2018!

## Slide 19
 | 52gMn | 52mMn | 51Mn
Half Life | 5.6 d | 21 m | 46 m
β+ Branch | 29% | 97% | 97%
β+ Avg. Energy | 242 keV | 1172 keV | 973 keV
Gammas | 744, 935, 1434, … | 1434 | 749

## Slide 20: 7Li(p,n) “Quasi-Monoenergetic” Neutron Source
Neutrons from 0-60 MeV
Y, Co, Al, In, Zr, Au samples irradiated in the vault
Unreacted beam dumped in Cave 0
Flux from 106-4 /MeV/sr/s (decreases w/En)
First experiments took place in April 2018
Inconel-clad Li targets
(LANL LDRD)
Jon Engle
Li(p,n) neutron
production target
Unreacted protons
Vault-based irradiation
0°
-20°
Notes: This is the same method used at the new FRANZ facility in Frankfurt.