## Slide 1
Two≈200 mg 93% 235U samples were irradiated at the LBNL 88-Inch cyclotron in 12 and 16 MeV deuteron beams
Deuterons @
12, 16 MeV
Stacked Target Holder
The 235U sample was “overfilled” with beam shifting “areal” distribution from target to beam
HPGe counter
Beam profile measured
Using GAFChromic film

## Slide 2
Post-irradiation counting shows the 642.3 keV g-ray from the decay of the 236Np isomeric state (t½=22.5 h)
Gamma-ray spectra from 235U foils irradiated at 12 MeV (top) and 16 MeV (bottom)
Neptunium-236g (t1/2=1.5 · 105 a) is used for IDMS determination of 237Np (t1/2=2.14 · 106 a).
238U(p,3n)236m+gNp experimental measurements show a 99.9 : 0.1 favoring of 237Np : 236gNp
The formation of short-lived isomer 263mNp (22.5h) generated via 235U(d,n) was quantified for two energies non-destructively after 60 minutes (16 MeV) and 9 hours (12 MeV) of deuteron irradiation at LBNL in August 2018.
Preliminary analysis shows EoB 235U(d,n)236mNp production yields of 29.95 kBq/uAh at 16 MeV and 5.15 kBq/uAh at 12 MeV.
236gNp and 237Np production cannot be quantified through decay spectroscopy: irradiated 235U foils have been shipped to LANL for ICP-MS analysis.
238U(p,3n)236m+gNp planned for Spring 2019, to measure the narrow 22 MeV <Ep< 27 MeV window for clean 236m+gNp production
Analysis underway by UCB postdoc Andrew Voyles

## Slide 3: The LBNL/UCB nuclear data group is characterizing the use of “secondary” neutron beams for isotope production
[1] K. P. Harrig, et al., “Neutron Spectroscopy for pulsed beams with frame overlap using a double time-of-flight technique,” NIM A, 877, pp. 359–366, 2018.
Produces a focused (~5°), intense (ϕn/ϕd≈ 3%) energetic secondary neutron flux (ESNF) from breakup of primary deuteron beam.
ESNF can be used to produce high specific-activity radionuclides via (n,2n), or charge exchange reactions such as (n,p) and (n,α).
Neutron volumetric range allows for trivial scale-up of production through increased target mass
Development supported under Research Development and Training in Isotope Production Proposal
Thick Be breakup target
≤ 50 MeV deuterons
Energetic secondary neutrons
(n,p) and/or (n,2n) target

## Slide 4: The LBNL/UCB nuclear data group is characterizing the use of “secondary” neutron beams for isotope production
First development run took place in August 2018: simultaneous production of 64,67Cu via energetic Zn(n,x), using 33 and 16 MeV deuteron breakup.
  64,67Cu are emerging as a “theranostic pair” for simultaneous dose delivery and imaging.
Preliminary analysis shows EoB production rates of 64Cu:67Cu in an approximately 75:1 ratio at 33 MeV and an 800:1 ratio at 16 MeV.
  Selection of deuteron energy allows co-production of 64,67Cu in a tunable ratio for applications!
  Complete analysis is underway and will form the master thesis for Ms. Nora Pettersen from the University of Oslo.
Irradiation of targets mounted at 0° to maximize neutron fluence
  Deuteron breakup neutrons have an energy-angle correlation – the spectrum “hardness” varies with angle off-axis
  This provides a second “tuning knob” for the 64Cu:67Cu ratio!
  Experiments in November 2018 and Feb 2019 will better characterize the angular breakup neutron spectrum
0°
5°
10°
15°
20°
30°
40°
60°
50°
Be breakup target
position
Zn
Target + monitor foils
6 mm Be breakup target
n
64Cu
67Cu
Notes: Mention issues with Levkovski!
Low peak is 54Fe(p,x), high peak is 56Fe(p,x)

## Slide 5: We are also addressing the need for non-standard PET tracers: natFe(p,x)51,52Mn – Novel PET imaging
Emerging medical radionuclides
  51Mn (t1/2 = 46 min, 97% β+) – short-lived PET tracer for metabolic studies
  52gMn (t1/2 = 5.6 d, 29% β+) – long-lived PET tracer for neuron tracking, immune studies
Two overlapping stacks: Ep= 5515 MeV, 250 MeV (120 nA@10 min, 100 nA@20 min)
Measurements across wide ranges of energy and product mass provide ideal inputs for improving predictive capabilities of reaction modeling
Precision excitation functions
Behavior of excited nuclear states
Multiple independent reaction channels
Notes: Mention issues with Levkovski!
Low peak is 54Fe(p,x), high peak is 56Fe(p,x)

## Slide 6
Project | Status | Degree
Fe(p,x)51,52m,52gMn | Manuscript Preparation | PhD, MSc
Zn(n,x)64,67Cu | Analysis Underway | MSc
Ir(d,x)193mPt | Scheduled: Feb 2019 | MSc
La(p,x)134Ce | Manuscript Preparation | PhD
235U(d,x)236mNp, Tm(d,x)169Yb | Analysis Underway | n/a
As(p,x)72Se,68Ge | Analysis Underway | PhD
86Sr(p,x)86Y, 86Sr(d,x)86Y | Scheduled: Feb 2019 | MSc
QMN Development | Analysis Underway | PhD
Since 2016, this student-led program has generated 1 PhD and 1 MSc, with an additional 3 PhD’s and 2 MSc’s in progress!
In addition to measurements, we train our students in dissemination of nuclear data to the user and evaluation communities  compiling each publication into EXFOR, including uncertainty analysis!
…as well as “Training and Retaining” the next generation…