## Slide 1: Isotope Production Activities Update
10 December 2018
Notes: Emerging trends for next-generation (targeted & personalized) nuclear medicine:
  Targeted alpha therapy (5-10 MeV)
    40-80 μm range  single cell
  Targeted Auger therapy (20 eV – 1 keV)
    1 nm – 2 μm  cellular nucleus
  Theranostic medicine
    Simultaneous imaging and therapy

## Slide 2: Stacked-target Charged Particle Excitation Functions
___________________________
Low(er) Energy – LBNL
Notes: Cyclotron
  Many hospitals have small K~15 medical cyclotrons for PET tracer production
  Leverage existing infrastructure
  Explore higher energies for regional research cyclotrons, basic science
Linac
  Commonly used for high-energy production (LANL – IPF)
  Useful for anchoring to complementary low-energy measurements

## Slide 3
 | 52gMn | 52mMn | 51Mn
Half Life | 5.6 d | 21 m | 46 m
β+ Branch | 29% | 97% | 97%
β+ Avg. Energy | 242 keV | 1172 keV | 973 keV
Gammas | 744, 935, 1434, … | 1434 | 749
Emerging medical radionuclides
  51Mn (t1/2 = 46 min, 97% β+) – short-lived PET tracer for metabolic studies
    Best option for clinical imaging, needs in-house production
  52gMn (t1/2 = 5.6 d, 29% β+) – long-lived PET tracer for neuron tracking, immune studies
    Long half-life, unfavorable gammas make this best-suited to pre-clinical imaging
    Easy distribution
  52mMn – short-lived PET tracer for metabolic studies
    Difficult to produce, must be done in-house
  Interesting lens to study behavior of excited states in p3/2 / f7/2 nuclei

## Slide 4: Stacked-target Charged Particle Excitation Functions
K-140
L. Bernstein
A. Springer
2016: Launched a complementary nuclear data measurement campaign at the LBNL 88-Inch cyclotron to address gaps in reaction data at E<60 MeV/A
Notes: We propose to measure these reactions to resolve ambiguity in the predictions and establish optimal irradiation parameters.
Cyclotron freq w = Q B / m
T = (m/2) w^2 r^2
T/A = (B r / 2 m)^2 (Q/A)^2 = K (Q/A)^2

## Slide 5: natFe(p,x)51,52Mn – Novel PET imaging
Two overlapping stacks: Ep= 5515 MeV, 250 MeV (120 nA@10 min, 100 nA@20 min)
Notes: Mention issues with Levkovski!
Low peak is 54Fe(p,x), high peak is 56Fe(p,x)

## Slide 6: natFe(p,x)51,52Mn – Novel PET imaging
Variance minimization:
55 MeV: +5.25% Al density
25 MeV: +6.69% silicone density
Notes: Mention issues with Levkovski!
Low peak is 54Fe(p,x), high peak is 56Fe(p,x)

## Slide 7: natFe(p,x)51,52Mn – Novel PET imaging
Measurements of 34 cross-sections for natFe(p,x), natCu(p,x), and natCu(p,x)
Notes: Mention issues with Levkovski!
Low peak is 54Fe(p,x), high peak is 56Fe(p,x)

## Slide 8: natFe(p,x)51,52Mn – Novel PET imaging
Two overlapping stacks: Ep= 5515 MeV, 250 MeV (120 nA@10 min, 100 nA@20 min)
Notes: Mention issues with Levkovski!
Low peak is 54Fe(p,x), high peak is 56Fe(p,x)

## Slide 9: As Targetry Fabrication

## Slide 10: Attempt 1 = Fail Too much distance Too much As2O3 in old stock Adhesive breaks down above 400°C
Result was films of As2O3 on receiver and intermediate on sight glass. However near source was nice film of pure As

## Slide 11
With two mini 500°C hotplates inside of vac chamber

## Slide 13
Success!!! (as of 4:54 AM…)

## Slide 14
Back to Berkeley…
Two deposition methods on 10um titanium foil:
  As2O3 (12.5 g/L) in 7M HCl, @ 130 mA
  As2O3 (0.2M) in 1:2 molar choline chloride : ethylene glycol deep eutectic solvent, @ 46 mA
Brass cathode
Stainless base + support
Platinum rod anode
Plating solution, in glass tube
Teflon o-ring
Backing foil
Teflon anode guide

## Slide 15
t0
t=2.5 h
t=2 h
t=0.5 h
t=1 h
t=1.5 h

## Slide 16
~6 mg/cm2
2.5 h @ 130 mA
~0.5 mg/cm2
15 m @ 30 mA

## Slide 17
Next steps
Characterization of all As targets
Continue fabricating electroplated As targets
  Pending new WPC approval
  Need relevant group members to take some more training
Start development of pressed-powder As targets
  As, As2O3, Cu3As, FeAs, Zn3As2…